## Slide 1: Maria’s Restaurant Chapter 1 Section 1

## Slide 2: System Design Process

## Slide 3: Manual N Commercial Load Calculation

## Slide 4: Load Calculation Factors
Typically, load calculations are simplified down to “total cooling tonnage per square foot of floor area”. This load calculation approach fails to take into consideration a variety of commercial building factors that greatly affect the choice of equipment and its capabilities, such as:

## Slide 5: Load Calculation Factors
Ventilation requirements: How much air must be brought in to meet safety and health related code requirements? How much makeup air is needed for exhaust systems for bathrooms and cooking equipment?
Commercial Equipment: What is inside generating a heat load? Commercial lighting, computer systems, ovens, dishwashers, refrigeration, laundry, etc.

## Slide 6: Load Calculation Factors
Windows: How many? What size? What is the frame type? Does the glass have any special qualities like a Low-e rating? Which direction do the windows face? How much internal shading (blinds, drapes, etc.) do they have? How much protection does the external shading from overhangs or porch roofs provide for the windows?
Skylights: What size? How many? What is the frame, glass and curb construction? Light shaft adjustment? What is the roof pitch where the skylights set? Which way do the skylights face (their orientation)?

## Slide 7: Load Calculation Factors
Door Traffic: What type of entrance doors are used and what is the frequency that they are opened and closed? Is there a shipping and receiving entrance that will be open often?
Number of People: How many people are in the building?
Insulation: Type and quantity in the walls, floors and ceilings (are all buildings really the same?)
Duct System: The location and design of the duct system can have a very large impact on the heating and cooling system size and efficiency.

## Slide 8: Load Calculation Factors
Outside Air: Will the fresh air makeup meet the requirements for the exhausted kitchen air in cooking areas and the outside air required by the size of the building and total occupancy.
Construction Materials: Is the building constructed from light-weight “stick built” or steel construction, versus heavy-weight masonry or concrete walls?
Construction Practices: How “tight” is the building? Were special products (air/water wrapped) or procedures (caulking, sealing) used to prevent excess energy loss?

## Slide 9: Manuals Referenced

## Slide 10: Rooftop Package Heat Pump

## Slide 11: Right Sizing
Unfortunately, too many “designers” opt immediately to use the largest rule-of thumb-values in such a scenario, resulting in oversized equipment and botched designs. Using a Pocket Guide to design a system is just plain lazy and inappropriate!

## Slide 12: Rules of Thumb

## Slide 13: Break The Rules and Pay a Price

## Slide 14: Load calculations vs the varying real time actual loads
Even when a contractor performs a proper load calculation, the procedure is done based on full occupancy, at design temperatures, when the hottest and coldest temperatures reached for 99% of the hours in a year at the buildings location. But what happens when it is not hot? Or not cold? What happens in the fall or spring when the temperatures are milder? What happens when the building is not fully occupied? All of the “over sizing” issues listed for oversized equipment can still happen.

## Slide 15: Gathering Load Calculation Data
For a building that is already built, a thorough inspection of the building that includes measuring walls, documenting room size, and building equipment, etc., is needed. For a building in a strip mall like Maria’s, the first thing needed for a load calculation is a drawing that has the floor plan. Ideally, the floor plan should include equipment types and locations, along with conditioned and unconditioned areas.

## Slide 16
Maria’s Restaurant Design
(Staff: Maria & 7 Employees each shift. Glass Store Front and front door)
66 ft.
25 ft.
F1
R1
S1
DW
C1
CT/O
C2
C3
SP
Fry
R2
F2
Woman’s
Restroom
1 handicap
1 standard
Men’s
Restroom
1 handicap
1 urinal
H1
Bar
Ice
C6
Counter
S3
C7
Bar 12 X 10
Seating 12
Restaurant 33 X 15
11 X 4 & 11 X 6
Seating 58
R3
R4
B1
Shelv.
S2
SK
B = Beverage Area R = Refrigerator (blue walk in
C = Counter S = Sink; S1 Hand; S2 3 Pot; S3 Bar
CT = 4 burner plus flat top over ovens SK= Steam Kettle
DW = Dishwasher SP = Salad/cold Prep table
F = Freezer (blue walk in) H1 = Hot Prep Table with Heat Lamp Shelf
Shelv..
Shelving/Storage
WH
S1
B2

## Slide 17: Block Load
A block load will often be completed for early, ballpark estimates during the bidding process. The block load only considers the building’s exterior walls, roof, and floors, and minimum code requirements.

## Slide 18: Room By Room Load
When awarded the job, a professional contactor will then perform a room-by-room heat loss/gain load calculations for each individual area in Maria’s restaurant. The area loads for individual rooms or sections are then totaled to show how much heating and cooling will be required for the entire building.

## Slide 19: Exhaust Totals (Work Sheet 1)
If you were provided with this table and did not have a code book available how would you determine the amount of airflow required if a piece of cooking equipment was removed and the kitchen exhaust hood size was changed to 10 linear feet?

## Slide 20: Design Value 1 In Linear Feet (Work Sheet 1)
If you were provided with this table and did not have a code book available how would you determine the amount of airflow required if the dishwasher hood size was changed to 4 linear feet?

## Slide 21: Design Value 2 In Linear Feet (Work Sheet 1)
If the two previous changes were made and the bathroom exhaust remained at 500 CFM, what would the new total exhaust be?

## Slide 22: Charbroiler Exhaust Totals (Work Sheet 1)
If an exhaust hood that was 11.5 linear feet long had the requirement of 550 CFM per linear foot due to extra heavy usage from because it covered a mesquite wood charbroiler, what would the exhaust fan total in CFM need to be?

## Slide 23: Field Notes
A brand new kitchen hood in a Chinese restaurant was not removing enough air resulting in smoke from the fryers and grilles getting into the cooking space.
Pulleys and belts were changed to increase the airflow: still not enough airflow out through the exhaust hood.

## Slide 24: Field Notes
Another Technician finally checked the exhaust fan motor for direction and found out it was running backwards.
The wiring was done by an electrician who did not know that a fan turning in the wrong direction moves less air.
The motor wiring was changed so that the fan rotation direction was reversed and the “problem” was resolved.