## Slide 1: Day 1 Part 1 Technician’s Guide & Workbook for Home Evaluation and Performance Improvement

## Slide 2: ACCA Standard 12
ANSI/ACCA 12 QH-2014 Existing Home Evaluation and Performance Improvement

## Slide 3: Comprehensive Performance Audit 3.0 1.0 Purpose; 2.0 Scope; 3.1 Interview

## Slide 4: Purpose
The Home Evaluation and Performance Improvement Standard establishes the minimum criteria by which deficiencies in existing residential buildings are identified by audit, improvement opportunities are assessed, scopes of work are finalized, work is performed in accordance with industry recognized procedures, and improvement objectives are met.

## Slide 5: Scope
The Home Evaluation and Performance Improvement Standard applies to site-constructed or manufactured one- and two-family dwellings and townhouses not more than three stories above grade in height.

## Slide 6: 3.0 Comprehensive Performance Audit Interview 3.1

## Slide 7: Comprehensive Performance Audit
Comprehensive performance audits collect information about the residence.
Measurements, tests, and observations are required to gather information for many areas of the home.

## Slide 8: Comprehensive Performance Audit
Comprehensive performance audits collect information about the residence.
Measurements, tests, and observations are required to gather information for many areas of the home.

## Slide 9: Interview
The interview is where the first information is gathered based on the homeowner’s opinion on how their home is operating and what their perceived performance problems are. Often they will think everything is OK and they are only seeking methods for reducing energy consumption.

## Slide 10: Interview

## Slide 11: Basic Interview Questions
    Do you own or rent the home? (Note: Renters must have express written permission from building owner prior to having an audit performed.)
    How many people live (or work) in this building?
    What year was your building built?
    How long have you lived there, and how long do you plan to stay?
    Of what improvements or changes in the building are you aware?

## Slide 12: Basic Interview Questions
    Do you have a set of building plans (architectural, as-built, material or equipment specifications or data sheets, etc.?)
6.

## Slide 13: Basic Interview Questions
Do you have high utility bill complaints?
Do you have complaints about condensation on windows, any plumbing or roof leaks, dripping ducts, or other building components including moisture problems near the foundation?
Do you have the last 12 months of utility usage (electric, gas, fuel oil, etc.) records or bills?

## Slide 14: Comfort Related Questions
Do you have any hot or cold rooms?
Do you have other comfort complaints? (Gather specific information: where in the building are they uncomfortable, the cause of discomfort: drafts, temperature, noise, and the remedy they use [e.g., covering a register, adjusting the thermostat, avoiding the room/space, etc.])
Where do you feel drafts or where is it drafty?

## Slide 15: Comfort Related Questions
How often do you open your windows instead of using the air conditioner to maintain comfort?
Do you have any indoor air quality issues?
Does anyone in the house suffer from health issues (allergies, asthma, temperature issues, odors/smells, etc.)?
Do you have any health related air filtration requirements?

## Slide 16: Comfort Related Questions
How often do you change the filter in the HVAC system(s)?
When was the last time you had the HVAC system checked for maintenance?
Do you know how to use the programmable thermostat?
Do you have a lot of dust in the house?

## Slide 17: Home Systems Utility Related Questions (appliances, lighting, water etc.)
Do you use compact fluorescent or light emitting diode (LED) light

## Slide 18: Home Systems Utility Related Questions (appliances, lighting, water etc.)
Do you turn on the kitchen exhaust fan when cooking?
Do you turn on the bath exhaust fan when bathing/showering?
Do you have a heated swimming pool? How is the pool heated? When do you use it? How long does the pump run? Is the swimming pool or spa inside your building? If so, how is that space ventilated?

## Slide 19: Combustion Safety Questions
Do you have any wood-burning stoves or fireplaces in the building? If so, how do you use them? Do they have outside air for combustion?
Do you have any unvented fireplaces or space heaters in the building? If so, how do you use them and how is combustion air provided during operation?

## Slide 20: Acceptable Documentation
Written or recorded responses for all of the 26 questions and for any follow up questions need to be kept in the job file.

## Slide 21: Math Review Basics

## Slide 22: Using Multiplication and Division

## Slide 23: Division
80 ÷ 5 = 16
Also written as:
5 80
1
5
3
0
6
30
0

## Slide 24: Multiplication and Division
6 x 5 x 4 = 120
4 x 6 x 5 = 120
10 ÷ 5 x 4 = ?
10 ÷ (5 x 4) = 1/2
(10 ÷ 5) x 4 = 8
(10 x 4) ÷ 5 = 8

## Slide 25: Multiplication and Division
0.56 x 0.35 = ?
0.56 x 0.35 = .196
0.56 ÷ 0.35= ?
0.56 ÷ 0.35 = 1.6
0.56 x 0.007 = .00392
0.56 ÷ 0.007 = 80
0.007 ÷ 0.56 = 0.0125

## Slide 26: Multiplication and Division
What is 6 feet 3 inches in feet?
1 foot = 12 inches
3 inches = 3 ÷ 12 = 0.25 feet
6 + 0.25 = 6.25 feet

## Slide 27: Area Calculations
For Squares and rectangles the area (A) is equal to length (L) x width (W) or A = L x W
Length
Width

## Slide 28: Area Calculations
A = L x W
Square L = W = 3
Length = 3
Width = 3
3 x 3 = 9 Square Something

## Slide 29: Area Calculations
For Squares and rectangles the area (A) is equal to length (L) x width (W) or A = L x W
Length = 3 feet
Width = 6 feet 3 inches

## Slide 30: Area Calculations
For Squares and rectangles the area (A) is equal to length (L) x width (W) or A = L x W
Length = 3 feet
Width = 6 feet 3 inches =
A = L x W = 3 x 6.25 = 18.75 square feet
6 + (3 ÷ 12) = 6.25 feet

## Slide 31: Area of a Circle
A = 3.14 x R x R
Radius = R
Diameter = 2 x R

## Slide 32: Area of a Circle
A = 3.14 x R x R
Radius = ½ D = 4 inches
Diameter = 8 inches
A = 3.14 x 4 x 4
A = 50.24 square inches

## Slide 33: Area of a Circle
A = 50.24 square inches
12 x 12 = 144
A in square inches = A in square feet
50.24 ÷ 144 = ?
0.3488888888888…

## Slide 34: Measuring Surface Area

## Slide 35: Area of a Triangle
For any triangle with a right angle the area is the length multiplied by the width (of the two legs meeting at the right angle) divided by 2.

## Slide 36: Area of a Right Triangle
For any triangle with a right angle the area is the length multiplied by the height of the two legs where the right triangle is divided by 2.
90o
90o
90o
90o
90o = right angle

## Slide 37: Area of a Triangle
For any triangle with a right angle the area is the length multiplied by the height of the two legs where the right triangle is divided by 2.
90o
90o
90o
90o
Length
Width

## Slide 38: Area of a Triangle
Length times width divided by 2.
90o
90o
90o
90o
Length 8’
Width 14’

## Slide 39: Area of a Triangle
Length times width divided by 2.
8 X 14 ÷ 2 = 56 Sq. Ft.
90o
Length 8’
Width 14’

## Slide 40: Area of a Triangle
A = hb X b ÷ 2

## Slide 41: Area of a Triangle
A = hb X b ÷ 2
90o
90o
b
hb

## Slide 42: Area of a Triangle
A = hb X b ÷ 2 =
90o
90o
b = 14’
hb= 6’
A = 6 X 16 ÷ 2 = 48 Sq. Ft.

## Slide 43: Area of a Triangle
Calculate the wall area for the following drawing:
8.0 ft
18.75 ft
3.66 ft

## Slide 44: Area of a Triangle
Calculate the wall area for the following drawing:
8.0 ft
18.75 ft
3.66 ft
8.0 ft X 18.75 ft = 150 ft2

## Slide 45: Area of a Triangle
Calculate the wall area for the following drawing:
8.0 ft
18.75 ft
3.66 ft
3.66 ft X 18.75 ft ÷ 2 = 34.3 ft2
hb
b

## Slide 46: Area of a Triangle
Calculate the wall area for the following drawing:
8.0 ft
18.75 ft
3.66 ft
34.3 ft2
150 ft2

## Slide 47: Area of a Triangle
Calculate the wall area for the following drawing:
8.0 ft
18.75 ft
3.66 ft
34.3 ft2
150 ft2
150 ft2 + 34.3 ft2 = 184.3 ft2