## Slide 1: Technician’s First Guide and Workbook Section 4: HVAC Maintenance Tools (1)

## Slide 2: HVACR Refrigerant Cycle Components
Most technicians will have the hand tools and testing tools required to do a basic HVAC system evaluation. One tool that is often overlooked by technicians is the manufacturer’s instruction package that is attached to every HVAC system that is shipped. The manufacturers spend a huge amount of money developing directions, to make sure every piece of equipment can be installed properly.

## Slide 3: MSDS Sheets
Access to materials safety data sheet (MSDS) for chemicals used and stored is a requirement; the best practice is to have them available on the service vehicles, and with the dispatcher who may receive an emergency call. The most important reason for reading MSDS sheets is for your own personal protection, and for the protection of others, you should read and understand the MSDS sheets that are available for all the chemicals and refrigerants you use.

## Slide 4: R-600a MSDS
Chemical Product and Company Identification
Composition / Information on Ingredients
Hazards Identification
First Aid Measures
Fire Fighting Measures
Accidental Release Measures
Handling and Storage
Exposure Controls/ Personal Protection
Physical and Chemical Properties
Stability and Reactivity
Toxicological Information
Ecological Information
Disposal Considerations
Transport Information
Regulatory Information
Other Information

## Slide 5: Personal Protection
Contact with chemicals is impossible to avoid when working on HVAC systems. Minimizing personal risk is the responsibility of the individual technician. Business have policies on reporting incidents, and the technician should be familiar with those policies. Those policies are for the good of the technician, and not following company procedures will put a technician at more risk. Technicians should wear a face shield or goggles for many maintenance and servicing tasks and use impervious insulated gloves to protect their hands when opening and closing refrigerant systems. In many shops, steel toed shoes or boots are required.

## Slide 6: Organizing Hand Tools
The type of work you do daily dictates the best set of hand tools you should carry and how they should be organized and transported. Three common ways of transporting the hand tools used in HVAC: tool boxes/bags, too buckets, and tool belts.

## Slide 7: Tools Sorted By The Job Type
Many technicians will have tools sorted into groups and may have a basic belt for basic equipment inspection work and a larger specialty assortment of tools organized in a bucket or box/bag sorted for specific jobs like servicing or installing the equipment. When working on equipment, taking the time to search for the proper tool is better than using the wrong tool. However, the best option is to have the correct tools organized so they can be found immediately.

## Slide 8: How Do The Experienced Techs Do It?
Looking at the tools other successful technicians have, and how they have them organized can help new technicians adapt to a company culture faster. For example, if tools are set up the same in tool boxes, or on trucks, technicians can help each other more easily when working in teams on large jobs. If every truck is laid out completely differently and contains tools in unique locations, it is a time-consuming task for someone to look on someone else’s truck for a tool. Worse yet, they are very likely to put them back into the wrong spot where they will be well hidden or even considered as lost or left behind.

## Slide 9: Basic HVAC Hand Tools
In this section tools that should be found in an entry level HVAC technician’s tool bag or belt will be reviewed. Measurement tools will be included in this section. However, instructions for their usage will be provided in the next chapter. An important tool is a small flash light that can be used to peer into dark areas. A box cutter is needed for opening boxes. Another tool often overlooked on tool lists is a way to write down part numbers and make notes: a pen and a writing pad (theses may be kept in a shirt pocket too an extra set is a good practice).

## Slide 10: Screw Driver and Nut Driver

## Slide 11: Screw Driver and Nut Driver

## Slide 12: Screw Driver and Nut Driver

## Slide 13: Adjustable Wrench
Adjust Opening
Turn Wheel

## Slide 14: Locking Adjustable Wrench
Adjust Opening
Turn Wheel
Squeeze Handle
Lock In Position

## Slide 15: Self Adjusting Wrench
Squeeze Handles
Together

## Slide 16: Hex (6 Sides) Wrench Set

## Slide 17: Screw-Bolt Removal Keys

## Slide 18: Side Cutter & Wire Skinner

## Slide 19: Lineman Pliers & Needle Nose Pliers

## Slide 20: Pliers That Adjust Opening Size

## Slide 21: Lessons Learned
You should now be able to identify types of adjustable tools used for removing and tightening bolts.
You should now be able to identify a wire skinner and explain what it is used for.
You should now be able to explain what a MSDS is and why it is important to know what is on one.
You should now be able to explain why it is important to select the correct size screw driver or nut driver and hex wrench.