## Slide 1: Technician’s First Guide and Workbook Section 21: Maintenance Inspection Basics (5)

## Slide 2: Boiler Combustion Venting
These tasks apply to gas and oil boilers and are not required for electric boilers:
Inspect vent piping and connections note any blockage, water corrosion, or signs of cracks or leaks.
Verify proper support and slope for vent piping.
Report and/or remove combustible materials placed too close to vent piping.

## Slide 3: Gas Boiler Combustion (1)
These tasks apply to gas boiler combustion system inspections:
Inspect burner for blockage and/or signs of moisture damage or corrosion.
Test inducer fan motor and blower assembly.
Inspect Heat Exchanger for signs of corrosion, fouling, and structural problems (cracks, bulging, holes). Measure and record temperature across the heat exchanger.
Look for signs of corrosion on the burners

## Slide 4: Gas Boiler Burner Assembly (1)

## Slide 5: Gas Boiler Burner Assembly (2)

## Slide 6: Gas Boiler Combustion (2)
Check igniter with an ohm meter inspect for cracks verify spark gaps are correct.
Measure and record inlet gas pressure adjust manifold as necessary.
Inspect ceramic flame probes for cracks.
Test main burner for ignition safety and for flame sequence.
Verify the combustion air is set properly.
Perform a combustion test.

## Slide 7: Inlet Gas Pressure Test Kit

## Slide 8: Oil Boiler Combustion (1)
These tasks apply to oil boiler combustion system inspections:
Inspect combustion chamber for cracks or structural damage.
Inspect Heat Exchanger for signs of corrosion, fouling, and structural problems (cracks, bulging, holes). Measure and record temperature across the heat exchanger.
Inspect burner gaskets.
Replace oil nozzle, verify size and spread.
Inspect oil nozzle head, electrodes and ceramic insulation and verify spark gap and positioning.

## Slide 9: Oil Nozzle & Oil Igniter Assembly

## Slide 10: Oil Boiler Combustion (2)
Measure and record photo-cell (cad-cell) resistance.
Replace fuel Filter
Measure and record oil pressure.
Test burner motor and assembly for correct operation.
If air is suspected of being in the oil line: bleed oil line until the air is removed.
Inspect oil pump and lines for signs of leaks.
For systems with a return line verify the oil is returning to the tank.

## Slide 11: Oil Filter

## Slide 12: Oil Boiler Combustion (3)
Measure and record ignition transformer’s secondary voltage (see Figure 104).
Perform and record results for a combustion analysis.
Measure temperature difference across the heat exchanger.
Verify primary burner control safety timing is within OEM specifications.

## Slide 13: Electric Boiler
These tasks apply to electric boiler system inspections:
Measure and record water temperature in and out and verify that the temperature range is within normal operating range.
Test sequence of operation.
Measure and record voltage amperage foe each heating element/circuit.

## Slide 14: Summary
If you come across something you have never see or are not sure of when performing a maintenance inspection never hesitate to call in to the shop or another technician with a question. Every HVAC manager and company owner would rather field dozens of questions than face one mishap, or job gone from small to large due to a technician’s error or lack of understanding. In today’s world of cell phones with cameras attached there is no excuse for not finding out the correct course of action before guessing at a solution.

## Slide 15: Summary
If you come across something you have never see or are not sure of when performing a maintenance inspection never hesitate to call in to the shop or another technician with a question. Every HVAC manager and company owner would rather field dozens of questions than face one mishap, or job gone from small to large due to a technician’s error or lack of understanding. In today’s world of cell phones with cameras attached there is no excuse for not finding out the correct course of action before guessing at a solution.

## Slide 16: True Story

## Slide 17: Lessons Learned
You should now know the steps required to verify that viable vent pipe is installed correctly.
You should now be able to explain why there is an oil filter on oil burner systems and why they need to be checked.
You should now be able to explain why an annual inspection is needed on Electric, and fossil fuel boilers.