## Slide 1: Major Hazards in LEO From Decaying Internet Satellites
Kenneth J MacLeod, member spst, kenmacleod@earthlink.net
Dr. James A Martin, Boeing (ret.), jamesamartin5@outlook.com
AIAA OC Chapter ASAT Conference, october 10, 2020

## Slide 2: The Questions
How many satellites would all the projected Internet constellations lead to, in total?
How many of those satellites would be decaying downwards towards re-entry, at any given time?
How will they impact the safety of the ISS, its replacements, and other high-value satellites in low Earth orbit?
What action, if any, is needed?

## Slide 3: How Many Internet Satellites in Total?
The total is approximately 100,000 satellites:
  Up to 42,000 from SpaceX
  Up to 48,000 from the new reborn OneWeb
  Up to 3,236 from Bezos’ Project Kuiper
  Up to 2,956 from Boeing
  Up to 292 from Telesat
  Up to 108 from LeoSat
  The numbers above are based on actual requests to the US FCC and other regulatory agencies

## Slide 4: Starlink Launch of 60 Satellites Ready to Deploy
Currently launching 60 satellites on each Falcon 9 rocket.
Later, potential to launch much larger batches on Starship/Super Heavy rocket.
Credit: SpaceX

## Slide 5: Simplified Calculation of Number of Decaying Internet Satellites
D = (N / L) x TL + N x F x TF
Where:
D = average number of decaying Internet satellites at any time
N = total number of active satellites in Internet constellations at completion
L = average life of satellites in years
TL = average time in years to decay to re-entry after end of life
F = average failure rate per year
TF = average time in years to decay to re-entry after failure on orbit

## Slide 6: What are the Values of the Parameters?
  N = 100,000 Internet satellites, approximately
  L = 5 years
    SpaceX estimates 3 to 5 years life on orbit; we use 5 years
  TL = 0.7 years, approximately
    SpaceX estimates several months to de-orbit; we use 0.7 years
  F = 0.02 estimated
    We estimate 2% failure rate on orbit per year
  TF = 3 years, approximately
    SpaceX estimates 1 to 5 years to re-entry after failure; we use 3 years

## Slide 7: How Many Satellites Decaying to Re-entry at Any Given Time?
D = (N / L) x TL + N x F x TF
D = (100,000 / 5) x 0.7 + 100,000 x 0.02 x 3
D = 14,000 after end of life + 6,000 after failure
D = 20,000 decaying Internet satellites

## Slide 8: How Much Control of Decaying Satellites?
Only limited low-acceleration ion propulsion after end of life:
Not adequate to evade collisions, even with warning
  At end of life, uses most of remaining propellant for de-orbit ‘burn’
Expected to retain some attitude control
  May be responsive and transmitting an ID signal
No propulsion or attitude control after failure on orbit:
  No method to evade collisions, even with warning
  May be tumbling and unresponsive after failure

## Slide 9: ISS and Successors Are at Risk of Collisions
For example, Starlink satellites are 570 lb or 260 kg each
Any impact could be catastrophic
Credit: NASA

## Slide 10: Major Hazard to ISS and Successors
Decaying Internet satellites will be collision hazard everywhere in LEO:
  ISS at 51 degrees inclination
    All Starlink orbital rings at 53 degrees inclination, for example
      Therefore, ISS at risk at all latitudes of its orbit
  ISS at 400 km altitude
    All Internet constellations will orbit above 400 km altitude
      Therefore, all Internet satellites will decay through ISS altitude
  Higher major-constellation LEO rings up to 630 km altitude
    Therefore, successors or ISS may be forced up to 650 km altitude or above

## Slide 11: Serious Risk of Debris Proliferation from Multiple Collisions
Highest risk is collisions of active or decaying Internet satellites with each other:
  Internet satellite rings in multiple planes intersect at numerous locations
  Decaying units in multiple rings will also intersect
  Decaying units will pass through active lower altitude satellite layers
  High potential for collisions at any of these intersections
In such dense rings, debris fragments from early collisions could result in further collisions

## Slide 12: Intersections of Multiple Rings of Internet Satellites Lead to Risk of Collisions with Decaying Satellites
Image repurposed to illustrate intersections concept.
This image actually shows final orbits of NASA UARS satellite before uncontrolled re-entry.
Credit: Universe Today

## Slide 13: Kessler Syndrome
An initial collision creates cloud of debris of various sizes
Debris fragments then collide with additional satellites
Leads to runaway chain reaction of numerous collisions
Resulting debris clouds prevent any further use of LEO for years to come
Credit: IEEE Spectrum

## Slide 14: Potential Solutions for Reducing Damaging Collisions or Kessler Syndrome
There are only a few alternative solutions:
  Greatly reduce the number of Internet satellites
  Much more rapid de-orbiting after satellite end of life
  Redundant systems to greatly reduce failure rate on orbit
  Watchdog timer and backup control to de-orbit when failure detected
  Buddy or cleanup satellites in each ring to rapidly de-orbit failed satellites
Each method is feasible
  But each increases cost and complexity for Internet providers
  Develop solutions now to avoid events which damage or delay this service

## Slide 15: Analysis and Agreements or Regulations to Reduce Collisions are Needed Soon
Today, only the FCC and the FAA provide some regulation for approval of constellations, based on radio band allocation and launch safety versus aircraft in the launch area, respectively. However, the FCC rules do include some limits on de-orbiting time, suitable for much smaller constellations.
Agreements or regulation need to take potential collisions in orbit into account
In addition, further regulatory considerations might include:
  Limiting brightness, to avoid interfering with general astronomy
  Limiting interference with surveys for potentially hazardous NEO asteroids

## Slide 16: Consider a Collision Risk Management Fee
The space in LEO has been considered unlimited and free
Over the decades since Sputnik I in 1957, there has been space for all
Collisions have been very rare
But this situation will change dramatically with 100,000 Internet satellites
Consider a risk management fee for each launch, depending on risk analysis
Much like insurance premiums
Funds reserved for tracking, cleanup, and replacement of damaged satellites
May require international agreements

## Slide 17: Conclusions
The total number of Internet satellites being planned for the large constellations is about 100,000.
The total number of Internet satellites decaying downward towards re-entry after end of life or failure on orbit will be about 20,000 at any time.
Such large numbers of decaying satellites with limited or no control will pose a major hazard of collision with the ISS or its successors, and may even lead to a runaway Kessler Syndrome, denying further access to LEO.
Analysis and agreements or regulatory action are needed very soon to limit the potential damage, either by greatly reducing the allowed numbers of satellites, or by de-orbiting the satellites much more rapidly after end of life or failure, or both.

## Slide 18: Thank You!
Major hazards in Leo from decaying internet satellites