## Slide 1: Leveraging an Experimental Database to Inform an OMARS Designed Experiment
Presented by
Peili Wang, Associate Director
Portfolio Statistics, Pfizer
NCB 2025

## Slide 2: General Bioprocess Flow for Drug Substance
Centrifuge
Clarification
Protein A
TMAE
Vpro VRF
UF/DF
Filtration
Low pH VI
pH adj Neut
Purification
Vial Thaw
Shake & Culture Bag Expansion
Bioreactor
Production Bioreactor
Bioreactor
Cell culture

## Slide 3: Outline
Building an experimental DoE database
  Combining Studies for Any Process Step: Challenges
  Prepare Database
  Dashboard: Data to Knowledge
Using the Database to Inform OMARS Design
  DoE Request
  Leverage database to inform design choices
Objective: turning historical datasets into knowledge

## Slide 4: Building a Historical Database
  Combining Studies for Any Process Step: Challenges
  Prepare Database
  Dashboard: Data to Knowledge

## Slide 5: Combining Studies for Any Process Step: Challenges
Dimensions
Studies/ Molecules / Compounds
Difficulties: Inconsistency cross studies
Not all compounds study the same attributes.
Outputs / Attributes / Y variables
Each attribute variation could be different
Not all compounds study the same process parameters within the same ranges.
Different design resolution
Data formatting issues: names, units.
Inputs / Process Parameters / Factors / X variables

## Slide 6: Prepare Database and Dashboard in Dataiku
A set of tables including data, factor information, and selected models.
One study: Format the files
Compile studies in Dataiku
Setup KEYS for process parameters and attributes (with scientists) and add into each study.
Make unit consistency: (e.g. mL or L).
Ability to extract: coefficients, effect size, standard error, R-squared,…etc.
Example of record selected models
Dashboard

## Slide 7: Dashboard: Data to Knowledge
Studied ranges for all factors.
Data range for all attributes.
Frequency about factors and attributes are studied.
Relative frequency of statistical significance
      Main effects
      Second order effects (Interaction, Quadratic)
Effect size (factors vs attributes)
Co-significant effects
Design:
Which factors were studied?
What were the factor ranges?
Which factors are most important? (effect size, frequency of significance)
Do we expect to see any interaction or quadratic effects?
Modeling:
Is the data range typical for the attributes?
Have we seen this effect in other studies?
FAQ
What the database can answer

## Slide 8: Dashboard: Data to Knowledge
One attribute in one study has one model.
UI to selected studies, factors, attributes

## Slide 9: Dashboard: Data to Knowledge
Study range for a factor cross studies
This visualization is available for # of studies, # of significance, or effect size.
Impact of factors for attributes
For second order effects (SOE)
co-significant with other SOE effects

## Slide 10: Using the Database to Inform OMARS Design
  DoE Request
  Leverage database to inform design choices

## Slide 11: Request 24-run study with 6 factors
Objective: Process characterization study
Restriction: 24-run design for six factors (27 effects) to ensure a single “block”.
Design Options
Central Composite Design (CCD)
Box-Behnken Design (BBD)
OMARS family: bridges the gap between Definitive Screening Design (DSD) and CCD

## Slide 12: OMARS design
Núñez Ares, Goos 2020 & Núñez Ares, Schoen, Goos 2023
Orthogonal
Minimally
Aliased
Response
Surface
designs
Correlation Matrix for an OMARS Design with Four Factors
Features of OMARS:
Three levels for each factor (-1, 0, 1).
Each main effect is not correlated with any other effects.
Allow the estimation of partial or complete second-order effects models.

## Slide 13: Using the database to inform design choices
Not “equal information” for each factor.
From Design
Design Correlation matrix
From Database
Frequency of quadratic effect

## Slide 14: Using the database to inform design choices
Not “equal information” for each factor.
From Design
From Database
Design Correlation matrix
Principle: When correlation between two effects are high in the OMARS design, ​assign the factors so that the chance two correlated effects are co-significant is low based on historical data.​
co-significant with other effects

## Slide 15: Summary
DoE Database:
Combining historical DoE studies.
A dashboard is built to answer common questions for DoE and modeling.
Application of database to inform design choices:
OMARS is picked and historical knowledge was used to inform design choices.
Other potential use:
Historical knowledge may inform the model selection process.

## Slide 16: Reference
José Núñez Ares & Peter Goos (2020) Enumeration and Multicriteria Selection of Orthogonal Minimally Aliased Response Surface Designs, Technometrics, 62:1, 21-36.
José Núñez Ares, Eric Schoen & Peter Goos (2023) Orthogonal Minimally Aliased Response Surface Designs for Three-Level Quantitative Factors and Two-Level Categorical Factors, Statistics Sinica, 33:107-126.
ENBIS-23 Valencia Conference (10-14 September 2023): Tremendous Impact of the Very New and Promising OMARS DOE in Pharma Industry for Quicker Access to New Vaccines · ENBIS Conferences (Indico)
OMARS Designs Add-in: A Gateway to a New Family of Orthogonal RSDs (2022-EU-30MP... - JMP User Community

## Slide 17: Acknowledgements
Statistician
Aili Cheng
Brad Evans
Katie Brickey
Scientists
Paul A Thoday
Chao Ma
Franklin Eduardo Mejia Frias
Pfizer Digital
Adam Nieto