## Slide 1: Low-cost Sensor to Strengthen CyanoHAB Monitoring with New Gen Ocean Color Satellites for Underrepresented Regions
Chintan B. Maniyar1, Abhishek Kumar1, Keshav Raviprakash1,2, Mark A. Seferian2,3, Isabella R. Fiorentino1, Deepak R. Mishra1
1Center for Geospatial Research, Department of Geography, University of Georgia
2College of Engineering, University of Georgia
3AI institute for Advanced Optimization, Georgia Institute of Technology

## Slide 2: What are CyanoHABs?
https://www.smithsonianmag.com/smart-news/algae-are-turning-antarcticas-ice-green-180974960/
Credit: Dr. Susan Wilde
Cyanobacterial Harmful Algal Blooms
A distinct group of phytoplankton – over 3 billion years old
Adaptable to a variety of aquatic environments
Need nutrient rich waters and warm temperature to bloom
Toxic – neurotoxins and hepatotoxins

## Slide 3: Why should we study CyanoHABs?
Economic loss Over $5B/year (LG Sonic, 2023)
Public Health Hazards Over $10B/year (Anderson et al,)
Biodiversity Loss
https://www.ewg.org/interactive-maps/2019_microcystin/map/

## Slide 4: Remote Sensing of CyanoHABs
Visual detection is difficult - highly synonymous with green (non-toxic) algae
Remote sensing of CyanoHABs either with Phycocyanin (PC) or Chlorophyll-a (Chl-a) pigments
PC is unique to CyanoHABs and absorbs light strongly at 620 nm à PC concentration
Chl-a present in all phytoplankton bloom and used frequently as a proxy à Cyanobacteria Cell Density (CCD)

## Slide 5: Gaps in Global CyanoHAB Monitoring
Monitoring efforts and accessibility skewed towards Global North
Under sampled or developing regions – significant blind spots
Severe events go unreported
Why? Lack of affordable resources
Jones et al, 2024: 10.1088/1748-9326/ad6919

## Slide 6: Solution: A Low-cost Hyperspectral CyanoHAB Sensor
Although satellite data is free, in-situ radiometry data is always needed to validate satellite observations and model development
In-situ sampling is costly
  Logistics – boat, buoys etc.
  Sensors – sophisticated/industry-grade in-situ sensors are prohibitively costly (upto $100,000 (SVC inc., 2025))
  Training – special skills to operate sensors
Limits in-situ data collection in resource limited and developing regions
Maniyar et al., 2025 (under review in ACS ES&T Water)
CyanoHAB Satellite Maps: Sentinel-2/3; PACE; Landsat-8/9
Low-cost In-situ data

## Slide 7: Cyanosense 2.0: Design & Development
Maniyar et al., 2025 (under review in ACS ES&T Water)

## Slide 8: Cyanosense 2.0: Operation
Maniyar et al., 2025 (under review in ACS ES&T Water)

## Slide 9: Does it really work? US-wide Testing
We visited 6 CyanoHAB prone lakes across the US in Summer 2024 to test Cyanosense 2.0!
Cyanosense2.0 $1,300 (to evaluate)
Maniyar et al., 2025 (under review in ACS ES&T Water)
SVC 1024-HRi $70,000 (as reference)

## Slide 10: Radiometric Evaluation (in-situ)
Radiometric sensitivity in the CyanoHAB active region: 550 nm – 750 nm
Maniyar et al., 2025 (under review in ACS ES&T Water)

## Slide 11: Cyanosense 2.0: Satellite Validation
Maniyar et al., 2025 (under review in ACS ES&T Water)
Sentinel-3 (OLCI) PACE (OCI)

## Slide 12: Supporting Satellite-based CyanoHAB Monitoring
Maniyar et al., 2025 (under review in ACS ES&T Water)
Sentinel-3 (OLCI) PACE (OCI)
NDCI PC3 CI PCI

## Slide 13: How does Cyanosense 2.0 benefit us?
Fits easily into existing monitoring frameworks
  EPA CyAN, USGS, GEOHAB, NLA etc.
Promotes citizen science
Easily affordable by developing and underrepresented regions
  Bridges monitoring gaps at a global level
  Long-term ground data collection
  Satellite validation
Suitable for other water quality parameters as well
Limitations
  Radiometric sensitivity in NIR region

## Slide 14: Overarching Borader Impact/ Bigger Picture
In-situ data
Satellite Data (PACE, Sentinel-2/3, Landsat-8/9)
Early Warning Model: Geo-AI, QR-NN, Mixture of Experts
Global CyanoHAB Dashboard (opensource)
Access it here:

## Slide 15: CyanoTRACKER Project Website (app coming soon!)
See an algal bloom anywhere near you? Report it on our website and we will relay it on to the authorities!
You can also request a satellite-based CyanoHAB map of any location if you flag an ongoing bloom!
Access our website here!
Report a bloom/HAB!
Request a HAB-Map!

## Slide 16: Acknowledgements
ASPRS and ORNL
Field campaign
  Cleveland State University, University of Wisconsin-Milwaukee, Florida Atlantic University, Utah State University, Department of Environmental Quality
Funding Agencies
  NASA FINESST: #80NSSC24K0068
  NASA ESROGSS: #80NSSC23K125
Logistical Support and Contribution
  Jonathan Crowell, Aladdin Al-Khatib, Maggie Kurdle, Ranganadh Srivillibhutturu, Nancee Uniyal, Rajneesh Sharma

## Slide 17: Thank you for your attention!
Any comments/ questions/ suggestions are welcome!
chintanmaniyar@uga.edu
LinkedIn