## Slide 1: Hyperspectral data from NASA Airborne platforms at the ORNL DAAC
Scott M. Pearson, Michele Thornton, Yaxing Wei, and Rupesh Shrestha
Remote Sensing and Environmental Informatics Group, Environmental Sciences Division, Oak Ridge National Laboratory
April 24, 2025

## Slide 2: NASA DAACs: Distribute Earth Science data products
Serve scientists and data users
NASA’s Open data initiative
Findable, Accessible, Interoperable, Reusable
Science themes

## Slide 3: ORNL DAAC
Terrestrial ecology
  Field observations
  Airborne missions
  Orbital products
  Model code & results
https://daac.ornl.gov → https://www.earthdata.nasa.gov/centers/ornl-daac

## Slide 4: Airborne data support …
Airborne-field investigations, process studies
  ABoVE, Delta-X, BioSCape, GEMx
Orbital instruments: development, calibration-validation:
  MODIS/ASTER Airborne Simulator (MASTER)
Airborne science research
  Western Diversity Time Series, Greenhouse Gas
Airborne Platforms
  operate at range of altitudes: 260 to 26,200 m
  often deploy multiple instruments
Twin Otter
ER-2
Gulfstream III
B200
https://airbornescience.nasa.gov/aircraft
Notes: Platform Images source: https://airbornescience.nasa.gov/aircraft

## Slide 5: Example spectroscopy instruments
MODIS/ASTER Airborne Simulator (MASTER)
Airborne Visible / Infrared Imaging Spectrometer (AVIRIS)
  AVIRIS-Classic, AVIRIS-Next Generation (AVIRIS-NG), AVIRIS-3, …
Hyperspectral Thermal Emission Spectrometer (HyTES)
Portable Remote Imaging Spectrometer (PRISM)
AVIRIS-NG instrument
https://avirisng.jpl.nasa.gov
Radiance: electromagnetic radiation reflected or emitted by an object (brightness for specific wavelength); depends on illumination. Units: μW nm-1 cm-2 sr-1
Reflectance: ratio (light leaving) / (light striking); depends on the material observed. Units: 0 – 1.0

## Slide 6: MODIS/ASTER Airborne Simulator (MASTER)
  Spectral range : 460 to 12,879 nm (visible – thermal IR)
  Spectral resolution 50 bands, irregular intervals
  Whisk-broom scanner; 716 pixels, 2.5 mrad FOV
  Spatial resolution depends on distance from sensor to surface (i.e., altitude)
  Products:
    Atmospheric corrected emissivity
    Land surface temperature
MASTER quicklook (R 4000, G 2200, B 1600 nm)
Mosquito Fire, California; 2022-09-08
Emissivity
The Western Diversity Time Series will observe ecosystems and provide critical information on natural disasters such as volcanoes, wildfires, and drought.
Notes: Sources: https://asapdata.arc.nasa.gov/sensors/master/data/deploy_html/wdts_2022_summer.html, MASTERL2_2263000_10_20220908_2004_2018_V02-images.zip (emissivity)
The Western Diversity Time Series (formerly HyspIRI) will observe California’s ecosystems and provide critical information on natural disasters such as volcanoes, wildfires, and drought. It will provide a benchmark on the state of the ecosystems against which future changes can be assessed, as the instruments will be capable of identifying vegetation type and health.

## Slide 7: Airborne Visible / Infrared Imaging Spectrometer- Next Generation (AVIRIS-NG)
  Spectral range : 380 to 2,510 nm (visible – near IR),
  Spectral resolution 425 bands, 5-nm intervals
  Pushbroom scanner with 640 cross-track elements, 1.4 mrad FOV (greater spatial resolution)
  Applications
    plant diversity
    ecosystem functions
    soil type
    geology / minerals
    greenhouse gas
    cal/val for satellite instr.
AVIRIS-NG
MASTER
Notes: Image: ang20200708t192518_geo.jpg

## Slide 8: Radiance and reflectance data
Calibrated radiance data – Level 1B (L1B):
Radiance units: μW nm-1 cm-2 sr-1
Georeferenced swath data in HDF or netCDF format
    data in instrument coordinates: lines x samples along flight trajectory
    pixel size on ground varies f(parallax, terrain)
Corrected surface reflectance – Level 2 (L2):
Scaled reflectance units: 0.0 to 1.0
Orthocorrected in GeoTIFF, ENVI, or netCDF
  Terrain corrected with regular pixel size
  Atmospheric and BRDF corrections may be applied
Radiance: electromagnetic radiation reflected or emitted by an object (brightness for wavelength); depends on illumination.
Reflectance: ratio (light leaving) / (light striking); depends on the material observed.

## Slide 9: Swath data: georeferencing & rectification
flight path
Original data in instrument coordinates: lines x samples
Coordinates assigned to each pixel f(sensor-surface geometry, terrain)
Resampled to regular grid (some pixels are interpolated), GLT
Orthocorrected data
Raw data
Notes: AVIRIS-NG: ang20200708t192518. Left image is gray scale of single band (red). Right is RGB image from radiance values.

## Slide 10: Radiance file structure & formats
Calibrated radiance : μW nm-1 cm-2 sr-1
  Image cube – “instrument” coordinates: lines x samples
  Georectified image – matrix with regularly spaced pixels
Geolocation – per pixel: lon/lat or UTM coordinates
Geometric lookup table – relates instrument image cube pixels to rectified pixels; true vs. interpolated pixels
Observation parameters: sensor to surface geometry, solar geometry, surface slope & aspect
Notes: In graphic, white pixels are interpolated. The color gradient shows “line” from image cube.

## Slide 11: Ancillary files
Spectral calibration: wavelength centers, range, FWHM for each band
Quicklook images : RGB, high resolution or reduced resolution
KMZ for viewing in Google Earth or GIS import
  Polygon outline of imagery footprint
  Polygon with RGB quicklook overlay
Imagery footprint for
ang20200708t192518

## Slide 12: Flight line catalogs for AVIRIS family & MASTER
AVIRIS-Classic / -NG : Flight Line Geospatial and Contextual Data
  https://doi.org/10.3334/ORNLDAAC/2140
MASTER: Flight Line Geospatial Polygons and Contextual Data
  https://doi.org/10.3334/ORNLDAAC/2151
Indexed by date, location, flight metadata
  CSV, Shapefile, KMZ, GeoTIFF formats
Notes: https://daac.ornl.gov/cgi-bin/dataset_lister.pl?p=47

## Slide 13: Data discoverability and access
Access through NASA’s Earthdata search (search.earthdata.nasa.gov)
  Filter by instrument, project, date/time, spatial bounds
  Download and access options; Web-based user interface or API tools
Search example:
AVIRIS-NG products
from
Delta-X project

## Slide 14: Data access options
Direct download
AWS cloud access
Earthdata login required
https://data.ornldaac.earthdata.nasa.gov/protected/deltax/DeltaX_L2A_AVIRIS-NG_BRDF_V3/data/ang20210925t152304_rfl_brdf.hdr
s3://ornl-cumulus-prod-protected/deltax/DeltaX_L2A_AVIRIS-NG_BRDF_V3/data/ang20210925t152304_rfl_brdf.hdr

## Slide 15: Enterprise services
Search and download APIs through NASA’s CMR
  See https://nasa-openscapes.github.io/earthdata-cloud-cookbook/, https://www.earthdata.nasa.gov/data/tools/earthaccess
  Python, R, and MATLAB programming options
Subsetting and reprojection via OPenDAP and Harmony (https://harmony.earthdata.nasa.gov/)
  Combine data from different collections
  Select variables, transform data; reproject to preferred CRS
  Select output format: NetCDF, GeoTIFF, JPEG2000, JSON, ASCII
  Jupyter Notebook demo available.