## Slide 1
VALIDATION ACTIVITIES:
AN EXAMPLE OF CLEANING VALIDATION PROTOCOL
ISCT Lab Practice Committee
June 2021
Gloria Carmona Sánchez
Head of Quality Assessment and GMP Facilities.
Andalusian Network for the Design and Translation of Advanced Therapies
http://www.sspa.juntadeandalucia.es/terapiasavanzadas/index.php/en/

## Slide 2
CLEANING VALIDATION
CONCLUSIONS
VALIDATION ACTIVITIES
INDEX

## Slide 3
QUALIFICATION
CALIBRATION
VALIDATION
Ensures an INSTRUMENT works as expected, under specifications
Ensures EQUIPMENT works according to expectations, complying with the specifications
Ensures that a PROCESS is performed according to expectations, complying with the specifications
Applies to Processes and Systems

## Slide 4
Should reinforce good manufacturing practices
Be conducted in accordance with defined procedures
Results and conclusions should be recorded
to demonstrate the ability to provide, on a continuing and reproducible basis, homogeneous products according to quality specifications.
VALIDATION STUDIES
OBJECTIVE

## Slide 5
Significant changes to facilities, equipment and processes, which may affect the quality of the product, should be validated.
A risk assessment approach should be used to determine the scope and extent of validation.
All validation activities should be planned.
Key elements should be clearly defined and documented in a validation master plan.
CONSIDERATIONS IN VALIDATION PROCEDURES

## Slide 6
Validation policy
Organizational structure of validation activities
Summary of facilities, systems, equipment and processes to be validated
Documentation format
Planning and scheduling
Change control
Reference to existing documents
Validation Master Plan
Notes: What is a validation master plan? It is a document that includes…

## Slide 7
VALIDATION MASTER PLAN
VALIDATION PROTOCOL
CONDUCT VALIDATION PROTOCOL
VALIDATION REPORT
STEPS DURING VALIDATION

## Slide 8
VALIDATION PROTOCOL
a written protocol
how validation will be conducted
specifying
approved
reviewed
VALIDATION REPORT: Collect all data obtained after developing validation protocol
critical steps and acceptance criteria need to be included
CONDUCT VALIDATION PROTOCOL

## Slide 9
A report that cross-references the validation protocol should be prepared, summarising the results, commenting on any deviations observed, and drawing the conclusions reached, including recommending changes necessary to correct deficiencies.
Any changes to the plan as defined in the protocol should be documented with appropriate justification.
VALIDATION REPORT

## Slide 10: PROCESSES THAT COMMONLY NEED TO BE VALIDATED
Cleaning validation
Environmental validation
Material disinfection validation
Process validation
Sterilization validation
Aseptic process validation
Transport validation

## Slide 11
VALIDATION ACTIVITIES
CLEANING VALIDATION
CONCLUSIONS
INDEX

## Slide 12
CLEANING VALIDATION
the documented evidence that a given cleaning procedure removes contaminants, residues from previous product, and cleaning agents below a pre-defined threshold.
OBJECTIVE
to demonstrate that the cleaning process consistently meets the predefined acceptance criteria

## Slide 13
  Cleaning validation protocol should be described in a document which should cover:
CLEANING VALIDATION PROTOCOL
Detailed cleaning procedure
Sampling procedures
By swabbing and/or rinsing or by other means depending on the production equipment
The sampling materials and method should not influence the result
Acceptance criteria
Specific rationale for setting limits should be included
The selection of the equipment should be representative of the worst case scenario

## Slide 14
Personnel responsible for conducting the cleanup must be trained in cleaning techniques
A specific plan needs to be established accordingly
CLEANING VALIDATION PROTOCOL
ASPECTS IN A CLEANING VALIDATION PROTOCOL
DISINFECTANTS
CLEANING PROCEDURE
CLEANING INTERVALS
CONTROLS TO BE PERFORMED AND MONITORING THE RESULTS

## Slide 15
  The following considerations apply when designing the strategy:
The influence between manufacturing and cleaning should be taken into account to define dirty time for cleaning procedures
The influence between cleaning and use should be taken into account to define clean hold times for cleaning procedures
CLEANING PROCEDURE AND CLEANING INTERVALS

## Slide 16
A. HOW TO SELECT THE ADEQUATE BIOCIDE TO DISINFECT
The selection of an adequate biocide to disinfect surfaces of aseptic zones is not easy
Depending on the type of product, the grade of the zone and the risks, different biocides can be used
DISINFECTANTS

## Slide 17
bactericide
fungicide
sporicide
virucide
  GENERAL BIOCIDAL ACTIVITY
A. HOW TO SELECT THE ADEQUATE BIOCIDE TO DISINFECT
DISINFECTANTS

## Slide 18
ALCOHOL
(IPA y etanol al 70%)
BACTERICIDE
FUNGICIDE
QUATERNARY AMMONIUM
BACTERICIDE
FUNGICIDE
HYDROGEN PEROXIDE 3%
BACTERICIDE
FUNGICIDE
VIRUCIDE
VIRUCIDE
VIRUCIDE
HYDROGEN PEROXIDE 6%
SODIUM HYPOCHLORITE
BACTERICIDE
FUNGICIDE
VIRUCIDE
SPORICIDE (in some cases)
HYPOCHLOROUS ACID
BACTERICIDE
FUNGICIDE
VIRUCIDE (depending on concentration)
SPORICIDE
BACTERICIDE
FUNGICIDE
VIRUCIDE (depending on concentration)
SPORICIDE
HYDROGEN PEROXIDE + PERACETIC ACID
BACTERICIDE
FUNGICIDE
VIRUCIDE
SPORICIDE
B. EFFECT OF THE MOST COMMON BIOCIDES (ORIENTATIVE)
DISINFECTANTS

## Slide 19
ALCOHOL
BACTERICIDE
FUNGICIDE
QUATERNARY AMMONIUM
BACTERICIDE
FUNGICIDE
HYDROGEN PEROXIDE 3%
BACTERICIDE
FUNGICIDE
VIRUCIDE
VIRUCIDE
VIRUCIDE
HYDROGEN PEROXIDE 6%
SODIUM HYPOCHLORITE
BACTERICIDE
FUNGICIDE
VIRUCIDE
SPORICIDE (in some cases)
HYPOCHLOROUS ACID
BACTERICIDE
FUNGICIDE
VIRUCIDE (depending on concentration)
SPORICIDE
BACTERICIDE
FUNGICIDE
VIRUCIDE (depending on concentration)
SPORICIDE
HYDROGEN PEROXIDE + PERACETIC ACID
BACTERICIDE
FUNGICIDE
VIRUCIDE
SPORICIDE
B. EFFECT OF THE MOST COMMON BIOCIDES (ORIENTATIVE)
DISINFECTANTS
The sporicides have an oxidative and corrosive capacity on aseptic surfaces, so their use needs to be reduced to a minimum
Depending on the microorganism identified in your facility…the specific zone, grade….

## Slide 20
  The following aspects need to be described
CONTROLS TO BE PERFORMED FOR MONITORING RESULTS
Monitoring points need to be defined…where, when , why…
How to codify the samples
Action and alert limits need to be established
Where the results are going to be recorded…

## Slide 21
CONDUCT VALIDATION PROTOCOL
According to the approved validation protocol
Using the records previously defined
By the trained personnel

## Slide 22
  A report needs to be prepared including the following aspects:
CLEANING VALIDATION REPORT
Summary of the results
Any deviation observed
The conclusions reached
Recommended changes, if any, to correct deficiencies
Appropriate justification if any changes to the plan need to be done
The established dirty and clean hold times after validation
REVIEWED
APPROVED

## Slide 23
  All primary data need to be stored as part of validation report
CLEANING VALIDATION REPORT
Monitoring records
Disinfectants used during the cleaning validation
Any deviation occurred
People involved in cleaning procedure
Notes: Any primary data need to be stored

## Slide 24
VALIDATION ACTIVITIES
CLEANING VALIDATION
CONCLUSIONS
INDEX

## Slide 25
KEYS FOR SUCCESS
To identify the factors that influence the effectiveness of the cleaning process
Operators
Rinsing times
The worst case scenario should be used
Cleaning equipment
Cleaning agents used
Number of operators
Number of times operators must enter the facility
Everything needs to be defined prior to start
Protocol and records
Materials to be used
Cleaning agents to be used and rotation plan
Personnel trained
Equipment, facilities
CLEANING VALIDATION

## Slide 26
    Have a question? Want to share a suggestion?
    The Lab Practices Committee Laboratory Life Line forum is a great way to get in touch with your network for insight, collaboration and help!
https://my.isctglobal.org/forums/Default.aspx

## Slide 27: REFERENCES
Eudralex – Volume 4 Good manufacturing practice (GMP) Guidelines. Part IV – GMP requirements for Advanced Therapy Medicinal Products. https://ec.europa.eu/health/sites/health/files/files/eudralex/vol4/2017_11_22_guidelines_gmp_for_atmps.pdf
PIC/S Validation-Master Plan, IQ, OQ, non-sterile Process Validation, Cleaning Validation (PI 006-3) Sept 2007. https://picscheme.org/docview/3447