Society of Petroleum Engineers

Distinguished Lecturer 2017-2018 Lecture Season

Integrating Geomechanics With Operational Practices Improves

Extended-Reach Drilling Performance

See Hong Ong

Baker Hughes

Abstract

Extended-reach wells present difficult drilling challenges, which if inadequately understood and addressed can yield significant downside risks and extensive non-productive time (NPT). These challenges are mainly due to complex well designs that combine high-deviation and extended-reach wellbores with difficult geology and hostile environments. Understanding the challenges and developing solutions are important to deliver the well with the proper casing specifications for production purposes.

Geomechanically, due to their long reaches and high deviations, borehole instability and lost circulations are particularly dominant in the overburden shale sections of extended-reach and horizontal wells. However, a good understanding of the rock failure mechanisms and an innovative use of the wellbore strengthening techniques can mitigate these geomechanical challenges through integration with good drilling practices such as efficient equivalent circulating density (ECD) management and effective hole-cleaning strategies. In addition, the long open-hole exposure typically experienced in these wells can cause chemical, thermal and/or fluid penetration issues that can further complicate the difficult drilling conditions. These secondary influences further stress the importance of incorporating geomechanical understanding in drilling fluids formulation.

This presentation focuses on the geomechanical challenges of drilling extended-reach wells. It highlights the need to integrate geomechanical solutions with appropriate drilling practices, particularly solutions based on good understanding of the intricate relationship between borehole stability, lost circulation, ECD, hole cleaning and bottom-hole assembly (BHA) optimizations in overcoming the drilling performance limiters. A case history will be presented as an example.

Biography

See Hong Ong received his B.Sc., M.Sc. and Ph.D. degrees in petroleum engineering from the University of Oklahoma. He has more 30 years of world-wide experience in petroleum engineering and petroleum-related geomechanics research and applications. His professional career includes 17 years at Baker Hughes where he is serving in various advisory, technical and managerial capacities, and 17 years at PETRONAS where he had management and operational responsibilities.  See Hong serves on many SPE technical program committees and has recently received the Regional Technical Award in Drilling Engineering. See Hong holds several US patents and has many publications in petroleum geomechanics.